## Slide 1
Creating a Geospatial Map of Light Attenuation
from Suspended Sediment Plumes
Laura Ramirez
Notes: Creating a Geospatial Map of Light Attenuation from Suspended Sediment Plumes

## Slide 2
OVERVIEW
Importance of seagrass
Sediment Plumes and their effects
CMP Final Report - Previous data analysis of light logger capture
Steps for data collection and manipulation
Heatmap
Future research perspectives

## Slide 4: Sediment Plumes

## Slide 5: CMP OYSTER MARICULTURE
Measure potential sediment generation at cultivated oyster mariculture (COM) operations in TX
Apply knowledge to simulate sediment plumes with similar characteristics at test seagrass beds, to measure if there were impacts to the seagrass.
Light Intensity parameter collected

## Slide 6: Project Goals
Understand light intensity behavior on experimental sediment plumes
Tidy field data to be processed into RStudio
Manipulate data to visualize percent light attenuation
Compare percent light attenuation values through all experiments in an area through the development of a two-dimensional heatmap of percent light attenuation values

## Slide 7: METHODS

## Slide 8: Study Site
(San Jose Island Map Picture here)
Notes: The first Seagrass study site that was selected was located on the western side of San Jose Island Southeast from the Southern tip of Mud Island, near North Pass. Depth at this location varied by up to 14 cm across the entire plot (mean depth 40 cm). A study site map showing depths across the site is presented below. This site served as the seagrass study site with a sandy substrate. Halodule wrightii was the predominant species, spread in a uniform pattern and density across the entire experimental plot. The experimental plot was rotated to the Northeast with the baseline following the compass heading 30 degrees ~NE. This was done to match prevailing wind patterns in the area coming out of the Southeast. Weather forecasts and conditions for this site were obtained from using the Port Aransas (Inside) weather station on Willy weather.

## Slide 9: Experimental Design
Grid Layout
Tracks
Zones
Zone A
Zone B
Zone C
Track 1
Track 2
Track 3
300 ft
200 ft
200 ft
100 ft
50 ft

## Slide 10: Light Logger Setup
Top Logger
Bottom Logger 10cm off the bottom
Loggers have individual serial numbers going permanently to a specific pole (A-L)
Separated in depth by 13cm
Notes: Rebar placed inside PVC to hold upright
Peg inserted to lowest PVC to prevent turning due to currents

## Slide 11: 07-18-2022 Experimental Layout

## Slide 12: Raw Data Collected by Light Loggers

## Slide 13: Experimental Design
Coordinate System
Inverse on x axis
(0,0)
(200,0)
(100,0)
(300,0)
(0,200)
(100,200)
(200,200)
(300,200)
(0,50)
(0,100)
(300,100)
(300,50)
(200,100)
(200,50)
(100,50)
(100,50)
Notes: Facilitates defining light logger pole position

## Slide 14: Tidying Up Data for RStudio

## Slide 15: 07-18-2022 Experimental Layout

## Slide 16: File Paths for Individual Light Loggers
pole_legend.xlxs – Sheet 1 (data_lightloggers)

## Slide 17: Disturbance Timeframes
pole_legend.xlxs – Sheet 2 (disturbance_periods)

## Slide 18: Data Manipulation – Calculating Coordinates

## Slide 19: Data Manipulation – Calculating Coordinates
Notes: Image of all maps at once

## Slide 20: Data Manipulation – Percent Light Attenuation

## Slide 21: Data Manipulation – Percent Light Attenuation

## Slide 22: Data Manipulation – Percent Light Attenuation

## Slide 23
Data Manipulation – Percent Light Attenuation

## Slide 24
Data Manipulation – Percent Light Attenuation
Notes: 1 or various?

## Slide 25: Data Manipulation – Individual Heatmaps

## Slide 26: Data Manipulation – Individual Heatmaps

## Slide 27: Data Manipulation – Individual Heatmaps

## Slide 28: Data Manipulation – Compiled Heatmap
script

## Slide 29: RESULTS

## Slide 30: Compiled Heatmap

## Slide 31: DISCUSSION

## Slide 32: Light Attenuation Example 1
09-25-22 Disturbance 1 10:00 a.m.

## Slide 33: Light Attenuation Example 2

## Slide 34: Improvements
Dates with wrong information deleted
Net around disturbance area so floating debris does not cover light sensors

## Slide 35: CONCLUSION

## Slide 36: Lab Pictures

## Slide 37: Works Cited